Low Power IoT Architectures
IoT Sockets : Direct & Remote Terminals
CPU/ULP
IoT SoC
IoT Board
IoT DevKit
IoT Platform
cycles : stages : phases
IoT data/”power” compression
Principles and Practices

---
IoT : Direct & Remote Terminals
IP-Thing : Direct Terminal connected to INET via WiFi/4G/5G link
non-IP-Thing : Remote Terminal connected to INET via LoRa link and IoT gateway

---
IoT Sockets : @IP:port:channel
Direct Terminals know: IP address:Service port:Channel number
Gateways know: IP address:Service port
Remote Terminals know only: Channel number (identifier)

---
Direct Terminals and IoT Sockets
A channel contains fields (max.8) that may be interpreted as IoT data streams to be “compressed”.
Direct Terminals know: IP address:Service port:Channel number
plus: write and optionally read key
IoT Socket

---
Remote Terminals and IoT Sockets
Gateways know IP address : Service port
Remote Terminals know only Channel number (identifier)
IoT Socket

---
From IoT SoC to IoT Platform
ARM-M0
RISC-V, Xtensa: LX6,LX7
IoT Platform
EEPROM
USB, solar Converters,
Bus I/O, ..
IoT DevKit
ESP32C3
ESP32C6
ESP32S3
WiFi/BLE
Bus I/O,..
IoT Board
CPU
SoC
IoT
UART,I2C,SPI
sensors/actuators,
modems, solar panel, battery
supercapacitors, ..
IDF, IDE,
drivers,
libraries, firmware C/C++, µPython, ..
Power
Profiler

---
From Platform to Application
App 1
App 2
App N
IoT Architecture
IoT Services
IoT Platform
AI assisted - Generation/Development process

---
ESP32C3 IoT SoC
RISC-V : 5-stages pipeline
Serial interfaces: I2C, SPI, UART, I2S, ..
Radio: WiFi, BT/BLE
low power : deepsleep
RTC clock, memory, ..

---
Heltec – ESP32C3 board
USB/UART
ESP32C3 SoC
Serial interfaces: I2C, SPI, UART, I2S, ..
EEPROM (SPI)
WiFi/BT/BLE – 2.4GHz antenna

---
IoT DevKit – HT ESP32C3
HT ESP32C3 board
SPI interface
OLED display
I2C interface
UART interface
RFM95: LoRa module
GPIO interface
sx1276 modem

---
Platform – Thonny IDE
files
editor
terminal

---
Platform – Thonny IDE
µPython interpreter type
port to flash
firmware to flash

---
Power Profiler Kit 2 (PPK2)
BAT+
BAT-

---
Chat GPT development assistance
Prompt engineering
requests, descriptions, specifications, ..
non complete code, some errors, ..
LLM engine
ChatGPT, LLAMA,..
generic code
post-engineering
final code
feedback, completions, modifications, ..

---
Simple example
Prompt:
Write MicroPython code for ESP32 to switch on the signal (buzzer) on Pin 3 for 3 seconds. Then switch off the signal and go to deepsleep for 6 seconds.
from machine import Pin, deepsleep
import time
# Initialize the SIG pin
led = Pin(3, Pin.OUT)
# Turn on the SIG
led.value(1)
print("SIG is ON")
time.sleep(3)
# Turn off the LED
led.value(0)
print("SIG is OFF")
# Go to deep sleep for 6 seconds
print("Going to sleep for 10 seconds...")
time.sleep(0.2) # added to see the print
deepsleep(6000) # 6 seconds in milliseconds
Remark:
The code is correct, no post-engineering and/or feedback

---
Simple example – PPK2 diagram
Calculate the average current for a cycle with 600s low_power stage ?
(18*600+35000*3)/(600+3) = 192µA
low_power stage ~18µA
high_power stage ~35mA
~3s

---
IoT Labs – Session 1
Lab 1: Working with sensors and displays (I2C bus)
Example Prompts
Prompt:
With ESP32 that is programmed with MicroPython we use frequently I2C bus to connect the sensors. Explain the operations of I2C bus.
from machine import Pin, I2C
# Configure I2C
i2c = I2C(0, scl=Pin(9), sda=Pin(8)) # I2C bus 0 with custom pins
# Scan for I2C devices
devices = i2c.scan()
print("I2C devices found:", devices)
# Assuming a device is found at address 0x3C
device_address = 0x3C
# Write to the device
data_to_write = bytearray([0x00, 0xFF]) # Example data
i2c.writeto(device_address, data_to_write)
# Read from the device
num_bytes = 2
data_read = i2c.readfrom(device_address, num_bytes)
print("Data read:", data_read)

---
IoT Labs – Session 1
Lab 1: Working with sensors and displays (I2C bus)
Example Prompts
Prompt:
Write for ESP32 in MicroPython the function and module sensors.py with drivers for max44009 (luminosity) and sht21 (temperature, humidity) sensors operating over I2C bus. The function takes two arguments : sda, scl to specify the pins of I2C bus. It returns 3 values: luminosity,temperature,humidity=sensors(sda,scl).

---
IoT Labs – Session 1
Lab 2: Communicating with WiFi and IoT servers
Example Prompts
Prompt:
Write in Micropython for ESP32 a module (wifi_tools.py) with 3 functions related to WiFi: connect_WiFi(ssid,pass), disconnect_WiFi() and scan_WiFi().
Prompt:
Write MicroPython code - function for ESP32 to get WiFi configuration: IP, port, .. after a successful connection to access point.

---
IoT Labs – Session 1 – Lab 2
Prompt:
Write MicroPython programs for ESP32 to send and receive simple UDP datagrams with socket() functions
Prompt:
Explain the function and the use of NTP protocol and server.
Prompt:
Write micropython code for ESP32 using the generated wifi_tools.py module to read time from an external NTP server. Read the time in a 10 second infinite cycle. Note that the time must be synchronized only in the first cycle. Print the values of hour, minute, and second.

---
IoT Labs – Session 1 – Lab 2
Prompt:
Give simple example in micropython for ESP32 of the usage of RTC memory. The example provides a counter of the cycles built with deepsleep mode for 6 seconds. Print the value of the counter in each cycle.

---
IoT Labs – Session 1 – Lab 3
Prompt:
Write MicroPython code for ESP32 to connect to WiFi Access Point and to send (publish) MQTT message. The message contains readings from MAX44009 and SHT21 with sensors.py module. Use previously created wifi_tools.py module to connect to WiFi access point.
Prompt:
Write MicroPython code for ESP32 to send several sensor data values to ThingSpeak server. Use MAX44009 and SHT21 sensors – sensors.py . Use wifi_tools.py module predefined previously to connect to the WiFi and ThingSpeak.com server.

---
IoT Labs – Session 1 – Lab 2

---
IoT Labs – Session 1 – Lab 3 & Lab 4
Lab 3: Building Close Terminals and Gateways with MAC-WiFi
Lab 4: Long distance communication with Remote Terminals over LoRa radio links

---
IoT Labs – Session 2 - Lab 5 + Project
Lab 5 : AIoT - EDGE
Projects and Applications with advanced IoT boards